## Slide 1
Modeling and Analysis of Bus Scheduling Systems of Urban Public Bus Transport
Group 2
Ameyaw Kofi, Erique Wilson, Nematov Abdulkhodiy, Shrestha Kriti Bahadur
Anbessa City Bus Service Enterprise (ACBSE)

## Slide 2
Global urban passenger demand reached 8 trillion passenger-kilometers in 2022
And…
is projected to more than double to 17 trillion passenger-kilometers by 2050

## Slide 3
Buses exceed capacity (125% ) IN Peak Hours, affecting service quality. The average 640,000. daily passenger load
Low occupancy (below 20%) during durig off peak, resource wastage.
Fixed schedule not match demand variability. Daily coverage: 78,963 km, with 5,500 trips.
Major expenses stem from fuel, maintenance, and depreciation, impacting overall efficiency.
Overcrowding during Peak Hours
Inefficient Resource Allocation
Underutilization during Off-Peak Hours
High Operating Costs
Problem Understanding
690 Buses
600 small
90 large
110 Routes
93 significant
17 low demand
640.000
Passengers
Daily Demand: 640.000 Riders

## Slide 4: Vehicle Scheduling Problem
BUS T-I
BUS T-II
X 600
X 90
Riders Demand
640.000 Daily Users
93 Routes
Start and End of Route circuit
Bus Stops
Capacity
690 Buses
Routes
93 Routes, 138Km avg Length Over 78,000 km traveled daily.
Shift 1
Morning
Shift 2
Noon
Shift 4
Afternoon
Shift 3
Night
ST: Shift Time
RTT: Round Trip Time:
  T: Trip Factor → ST / RTT
MWT: Max Wait Time: 30 Mins
  Time between consecutive departures
Cost: Bus Type I : 2 x
Cost: Bust Type II: 3 x
RTT
Average Fleet Size: 534 buses daily.
Daily Passenger Volume: 640,000 passengers per day.
Total Number of Routes: 110 routes.
Peak Hour Services: Additional peak hour services are operated on 37 routes.
Average Distance per Bus: 138 km per day.
Average Trips per Bus: 61.50 trips per day.

## Slide 5
Shift | Time Interval | Duration (Min.) | Demand Proportion (%)
Morning Peak | 6:15-9:30 | 195 | 40%
First off-peak | 9:30-15:30 | 360 | 20%
Evening peak | 15:30-19:30 | 240 | 35%
Second off-peak | 19:30-21:00 | 90 | 5%
Total |  | 870 | 100%
Route | D1 | D2 | D3 | D4 | T1 | T2 | T3 | T4
1 | 1650 | 825 | 1444 | 206 | 7 | 12 | 8 | 3
2 | 1399 | 699 | 1224 | 175 | 4 | 7 | 5 | 2
3 | 4412 | 2206 | 3861 | 552 | 4 | 7 | 5 | 2
4 | 1212 | 606 | 1060 | 151 | 3 | 5 | 3 | 1
5 | 1404 | 702 | 1229 | 176 | 5 | 8 | 6 | 2
6 | 443 | 221 | 387 | 55 | 4 | 7 | 5 | 2
7 | 1404 | 702 | 1229 | 176 | 7 | 11 | 8 | 3
8 | 2009 | 1004 | 1758 | 251 | 7 | 11 | 8 | 3
9 | 1814 | 907 | 1588 | 227 | 4 | 7 | 5 | 2
10 | 292 | 146 | 255 | 36 | 6 | 10 | 7 | 3
11 | 497 | 248 | 435 | 62 | 3 | 5 | 3 | 1
12 | 346 | 173 | 302 | 43 | 6 | 10 | 7 | 3
13 | 216 | 108 | 189 | 27 | 5 | 8 | 6 | 2
Demand Dataset

## Slide 6
Objective Function | 
Minimize Z: Total Daily trips | 
Alternative Minimize Z: Total Daily Cost | 
Constraints | 
Demand Satisfaction | ∀i,j (1)
Bus Reuse Constraint | B1[i,j]×Tfactor​≥x[i,j] (2) B2[i,j]×Tfactor≥y[i,j] (3) where Tfactor=min(T[i,j],w[j]) ensuring buses can be reused efficiently during a shift.
Capacity | (4) (5)
Minimum service level | x[i,j]+y[i,j]≥w[j] (7)
Non Negativity | 
Objective Function | 
Minimize Z: Total Daily trips | 
Alternative Minimize Z: Total Daily Cost | 
Constraints | 
Demand Satisfaction | 
Bus Reuse Constraint | B1[i,j]×Tfactor​≥x[i,j] (2) B2[i,j]×Tfactor≥y[i,j] (3) where Tfactor=min(T[i,j],w[j]) ensuring buses can be reused efficiently during a shift.
Capacity | 
Minimum service level | x[i,j]+y[i,j]≥w[j] (7)
Non Negativity | 
Notes: Total daily operating cost. Since in the article there is no detail about Costs of operation per Bus Type, per Km, the selected approach is minimizing the number of trips needed to satisfy the Demand
Simply by using a cost factor per trip.
Constraints:
Demand Satisfaction:
This restriction ensures that the aggregated capacity of the available buses is sufficient to satisfy the demand on each route and shift.
Prevents overuse of buses and ensures that the number of buses assigned to a route and shift is sufficient for the required trips:
Fleet Availability: 600 Buses Type I and 90 Buses Type II.
Minimum Service Frequency, or Minimum number of trips per turn, must guaranty an 30 Minutes wait for all routes, where:
Non-Negativity: The number of trips by both bus Type-I and Type-II must be non-negative, as negative trips are not feasible.
Total daily operating cost. Since in the article there is no detail about Costs of operation per Bus Type, per Km, the selected approach is minimizing the number of trips needed to satisfy the Demand
Simply by using a cost factor per trip.
Constraints:
Demand Satisfaction:
This restriction ensures that the aggregated capacity of the available buses is sufficient to satisfy the demand on each route and shift.
Prevents overuse of buses and ensures that the number of buses assigned to a route and shift is sufficient for the required trips:
Fleet Availability: 600 Buses Type I and 90 Buses Type II.
Minimum Service Frequency, or Minimum number of trips per turn, must guaranty an 30 Minutes wait for all routes, where: 𝑤𝑗= (𝑇𝑜𝑡𝑎𝑙 𝐷𝑢𝑟𝑎𝑡𝑖𝑜𝑛 𝑓𝑜𝑟 𝑆ℎ𝑖𝑓𝑡 𝑗)/(30 𝑀𝑖𝑛𝑢𝑡𝑒𝑠)
Non-Negativity: The number of trips by both bus Type-I and Type-II must be non-negative, as negative trips are not feasible.

## Slide 7
Solver Used

## Slide 8
Some Coding Discussion

## Slide 9
Some Coding Discussion

## Slide 10
Some Coding Discussion

## Slide 11
Console Output

## Slide 12
Results Dataset

## Slide 14
Scenario | Demand (Riders) | Trips T1 | Trips T2 | Total Trips | Buses T1 | Buses T2 | Total Buses | Frequency (Mins) | Total Cost | Fare | Revenue | Profit
1 | 100000 | 5437 | 67 | 5504 | 1092 | 76 | 1168 | 15 | $ 1,107,500.00 | 5 | $ 500,000.00 | $ (607,500.00)
2 | 200000 | 5266 | 475 | 5741 | 1177 | 205 | 1382 | 15 | $ 1,195,700.00 | 5 | $ 1,000,000.00 | $ (195,700.00)
3 | 300000 | 6662 | 162 | 6824 | 1326 | 163 | 1489 | 15 | $ 1,381,000.00 | 5 | $ 1,500,000.00 | $ 119,000.00
4 | 400000 | 7294 | 566 | 7860 | 1525 | 265 | 1790 | 15 | $ 1,628,600.00 | 5 | $ 2,000,000.00 | $ 371,400.00
5 | 500000 | 7711 | 1165 | 8876 | 1677 | 246 | 1923 | 15 | $ 1,891,700.00 | 5 | $ 2,500,000.00 | $ 608,300.00
6 | 550000 | 8586 | 1028 | 9614 | 1714 | 258 | 1972 | 15 | $ 2,025,600.00 | 5 | $ 2,750,000.00 | $ 724,400.00
7 | 100000 | 2774 | 168 | 2942 | 685 | 158 | 843 | 30 | $ 605,200.00 | 5 | $ 500,000.00 | $ (105,200.00)
8 | 200000 | 3188 | 601 | 3789 | 868 | 302 | 1170 | 30 | $ 817,900.00 | 5 | $ 1,000,000.00 | $ 182,100.00
9 | 300000 | 5122 | 205 | 5327 | 1110 | 76 | 1186 | 30 | $ 1,085,900.00 | 5 | $ 1,500,000.00 | $ 414,100.00
10 | 400000 | 5672 | 831 | 6503 | 1336 | 270 | 1606 | 30 | $ 1,383,700.00 | 5 | $ 2,000,000.00 | $ 616,300.00
11 | 500000 | 7076 | 982 | 8058 | 1553 | 290 | 1843 | 30 | $ 1,709,800.00 | 5 | $ 2,500,000.00 | $ 790,200.00
12 | 550000 | 7569 | 1199 | 8768 | 1581 | 356 | 1937 | 30 | $ 1,873,500.00 | 5 | $ 2,750,000.00 | $ 876,500.00
13 | 555000 | 7425 | 1383 | 8808 | 1692 | 340 | 2032 | 30 | $ 1,899,900.00 | 5 | $ 2,775,000.00 | $ 875,100.00
14 | 100000 | 1245 | 584 | 1829 | 510 | 226 | 736 | 60 | $ 424,200.00 | 5 | $ 500,000.00 | $ 75,800.00
15 | 200000 | 2456 | 703 | 3159 | 755 | 270 | 1025 | 60 | $ 702,100.00 | 5 | $ 1,000,000.00 | $ 297,900.00
16 | 300000 | 3893 | 807 | 4700 | 991 | 211 | 1202 | 60 | $ 1,020,700.00 | 5 | $ 1,500,000.00 | $ 479,300.00
17 | 400000 | 4515 | 1493 | 6008 | 1241 | 329 | 1570 | 60 | $ 1,350,900.00 | 5 | $ 2,000,000.00 | $ 649,100.00
18 | 500000 | 6178 | 1497 | 7675 | 1486 | 358 | 1844 | 60 | $ 1,684,700.00 | 5 | $ 2,500,000.00 | $ 815,300.00
19 | 550000 | 7631 | 1083 | 8714 | 1592 | 333 | 1925 | 60 | $ 1,851,100.00 | 5 | $ 2,750,000.00 | $ 898,900.00
20 | 555000 | 7269 | 1412 | 8681 | 1640 | 346 | 1986 | 60 | $ 1,877,400.00 | 5 | $ 2,775,000.00 | $ 897,600.00
21 | 560000 | 6896 | 1700 | 8596 | 1676 | 360 | 2036 | 60 | $ 1,889,200.00 | 5 | $ 2,800,000.00 | $ 910,800.00
22 | 25000 | 711 | 61 | 772 | 375 | 156 | 531 | 120 | $ 160,500.00 | 5 | $ 125,000.00 | $ (35,500.00)
23 | 50000 | 639 | 291 | 930 | 400 | 193 | 593 | 120 | $ 215,100.00 | 5 | $ 250,000.00 | $ 34,900.00
24 | 100000 | 1214 | 382 | 1596 | 495 | 218 | 713 | 120 | $ 357,400.00 | 5 | $ 500,000.00 | $ 142,600.00
25 | 200000 | 2174 | 817 | 2991 | 749 | 328 | 1077 | 120 | $ 679,900.00 | 5 | $ 1,000,000.00 | $ 320,100.00
26 | 300000 | 4132 | 607 | 4739 | 1026 | 290 | 1316 | 120 | $ 1,008,500.00 | 5 | $ 1,500,000.00 | $ 491,500.00
27 | 400000 | 4641 | 1385 | 6026 | 1301 | 317 | 1618 | 120 | $ 1,343,700.00 | 5 | $ 2,000,000.00 | $ 656,300.00
28 | 500000 | 6323 | 1385 | 7708 | 1548 | 360 | 1908 | 120 | $ 1,680,100.00 | 5 | $ 2,500,000.00 | $ 819,900.00
29 | 550000 | 7434 | 1203 | 8637 | 1647 | 360 | 2007 | 120 | $ 1,847,700.00 | 5 | $ 2,750,000.00 | $ 902,300.00
30 | 555000 | 7225 | 1432 | 8657 | 1163 | 347 | 1510 | 120 | $ 1,874,600.00 | 5 | $ 2,775,000.00 | $ 900,400.00
31 | 560000 | 7290 | 1428 | 8718 | 1639 | 360 | 1999 | 120 | $ 1,886,400.00 | 5 | $ 2,800,000.00 | $ 913,600.00
32 | 562000 | 7256 | 1463 | 8719 | 1668 | 360 | 2028 | 120 | $ 1,890,100.00 | 5 | $ 2,810,000.00 | $ 919,900.00
Results Multiple Scenarios

## Slide 15
Profit Analysis for Service Level by Wait Time (Bus Frequency, 15', 30', 60', 120' )

## Slide 19: Questions…